DIVISION 08 - OPENINGS

SECTION 08 17 00 INTEGRATED DOOR OPENING ASSEMBLIES

Specifier Note: Coordinate and edit articles and paragraphs below to suit project requirements. Add section numbers and titles per CSI "MasterFormat" and specifier's actice. Consult with manufacturer regarding performance requirements for units applicable to project, as well as, related equipment and accessories required.

PART I – GENERAL

1.01 SUMMARY

A. 	WORK INCLUDED: Furnish exterior and interior power door operators with visible mounting, as specified, that has been manufactured, fabricated and installed to maintain performance criteria stated by manufacturer without defects, damage or failure. Automatic door operators shall be configured as follows:

1. 	Single doors: Outswing or Inswing.

2.  Simultaneous pairs: Outswing or Inswing.

B. 	RELATED WORK:

1.	Division 8 Section "Aluminum Doors and Frames" for entrances furnished separately.

2.	Division 8 Section "Door Hardware" for hardware to the extent not specified in this Section.

3.	Division 16 Section for electrical connections including conduit and wiring for power door operators.

1.02  REFERENCES

A.	AMERICAN ARCHITECTURAL MANUFACTURERS ASSOCIATION (AAMA) 101: Appendix Dissimilar Materials.

B. 	AMERICAN ASSOCIATION OF AUTOMATIC DOOR MANUFACTURERS (AAADM).

C. 	AMERICAN NATIONAL STANDARDS INSTITUTE (ANSI):

1. 	ANSI A156.19: For Power Assist and Low Energy Power Operated Doors

2. 	ANSI.117.1: Accessible and Usable Buildings and Facilities

D. 	AMERICAN SOCIETY FOR TESTING AND MATERIALS (ASTM) B221: Aluminum-Alloy Extruded Bars, Rods, Shapes and Tubes.

E. 	AMERICANS WITH Disabilities Act (ADA) 1990

F. 	BUILDING OFFICIALS AND CODE ADMINISTRATORS INTERNATIONAL (BOCA)

G.	INTERNATIONAL CONFERENCE OF BUILDING OFFICIALS / UNIFORM BUILDING CODE (ICBO/UBC)

H.	International Code Council / International Building Code (ICC/IBC)

I. 	NATIONAL FIRE PROTECTION ASSOCIATION (NFPA) 101:

1.	NFPA 101: Code for Safety to Life from Fire in Buildings & Structures.

2.	NFPA 70: National Electrical Code (NEC).

J. 	THE ALUMINUM ASSOCIATION (AA) Aluminum Finishes Manual.

K. 	UNDERWRITERS LABORATORY, INC. and CANADIAN STANDARDS ASSOCIATION (USA & CANADA)

1. UL 325: Electrical Door, Drapery, Gate, Louver, and Window Operators and Systems.

2. CSA 22.2-247: Operators and Systems of Doors, Gates, Draperies, and Louvres.

1.03  SUBMITTALS

A. 	PRODUCT DATA: Submit manufacturer's complete product and installation data.

B. 	SHOP DRAWINGS: Submit drawings showing layout, profiles, product components including anchorage, accessories, finish and glazing details (where required).

C. 	CLOSEOUT SUBMITTALS: Submit the following:

1. 	Owner’s Manual.

2. 	Warranty document as specified herein.

3. 	AAADM inspection compliance form completed and signed by certified AAADM inspector prior to doors being placed in operation as proof of compliance with ANSI A156.19.

1.04  QUALITY ASSURANCE AND PERFORMANCE REQUIREMENTS

A. 	INSTALLERS QUALIFICATIONS: Installer shall be factory trained, certified by AAADM, and experienced to perform work of this section.

B. 	MANUFACTURER’S QUALIFICATIONS: Manufacturer to have minimum (5) five years successful experience in the fabrication of automatic doors of the type required for this project. Manufacturer capable of providing field service representation during installation, approving acceptable installer and approving application method.

C.	CERTIFICATIONS: Automatic sliding door systems and options shall be factory certified to meet performance design criteria in accordance with the following standards:

1.	ADA 1990: Americans With Disabilities Act

2.	ANSI A156.19: For Power Assist and Low Energy Power Operated Doors

3. 	ANSI.117.1: Accessible and Usable Buildings and Facilities

4.	NFPA 101: Code for Safety to Life from Fire in Buildings & Structures.

5.	UL 325: Electrical Door, Drapery, Gate, Louver, and Window Operators and Systems.

6.  CSA C22.2-247: Operators and Systems of Doors, Gates, Draperies, and Louvres.

7.	BOCA: Means of Egress, Power Operated Doors

8.	ICBO/UBC: Egress Through Lobbies

9.	ICC/IBC: Egress Section

D.	SOURCE LIMITATIONS: Obtain automatic door operators through one source from a single manufacturer.

E.	Product Options:  Drawings indicate sizes, profiles, and dimensional requirements of automatic entrance door assemblies and are based on the specific system indicated.  Refer to Division 1 Section "Product Requirements."

F.	Power Operated Door Standard: ANSI/BHMA A156.19.

G. OPERATION: “Knowing Act” and/or Manual:

1. 	Knowing Act: Knowing Act activation device (Pushbutton/Push plate switch, touchless sensor, etc.) actuates door to open; door closes after time delay expires. Opening and closing force, measured 1" (25.4 mm) from the latch edge of the door, not to exceed 15 pounds (67 N) of force to stop the door when operating in either direction. Operator to include the following variable adjustments so as to comply with ANSI Standard A156.19: Opening time – 4 1/2 to 6 seconds; Closing time – 4 1/2 to 6 seconds.

2. 	Manual: Push-N-Go™: Manually pushing door activates automatic opening cycle; door closes after time delay expires (approximately 30% less than after pushbutton actuation).

H.	Electrical Components, Devices and Accessories:  Listed and labeled as defined in NFPA 70, Article 100, by a testing agency acceptable to authorities having jurisdiction, and marked for intended use.

I.	OPERATING RANGE: -30° F to 130° F (-34° C to 54° C)

J. 	OPENING FORCE REQUIREMENTS FOR Egress doors: In the event power failure to the operator, swinging automatic entrance doors shall open with a manual force, not to exceed 30 lbf (133 N) applied at 1” (25 mm) form the latch edge of the door.

K. 	DOOR ENERGY: The kinetic energy of a door in motion shall not exceed 1.25 lbf-ft (1.69 Nm).

L.	CLOSING TIME:

1. 	Doors shall be field adjusted to close from 90 degrees to 10 degrees in 3 seconds or longer.

2. 	Doors shall be field adjusted to close from 10 degrees to fully closed in not less than 1.5 seconds.

1.05  WARRANTIES

A. 	MANUFACTURER'S WARRANTY: Units to be warranted against defect in material and workmanship for a period of one year from the Date of Substantial Completion.

Manufacturer's warranty is in addition to, and not a limitation of, other rights owner may have under Contract Documents.

B. 	DISTRIBUTOR'S WARRANTY: One year warranty: Labor & transportation charges for defective parts replacement.

1.06  PROJECT CONDITIONS AND COORDINATION

A.	Field Measurements: Verify actual dimensions/openings by field measurements before fabrication and record on shop drawings.

B.	COORDINATION: Coordinate with fabrication and construction schedule to avoid construction delays.

1.	Coordinate with door, door frame, and hardware contractors to insure proper size, hand, and finish.

2.  Coordinate with electrical contractors for power, activate switch, and fire alarm wiring.

1.07 DELIVERY, STORAGE AND HANDLING

A. 	ORDERING AND DELIVERY: Comply with factory's ordering instructions and lead time requirements. Delivery shall be in factory's original, unopened, undamaged containers with identification labels intact.

B. 	STORAGE AND PROTECTION: Provide protection from exposure to harmful weather conditions and vandalism.

PART ll - PRODUCTS

2.01  MANUFACTURER

Horton Automatics, a division of Overhead Door Corporation, shall manufacture automatic swing door(s) of type(s) and size(s) specified on plans and door schedule.

2.02  EQUIPMENT

A. 	MANUFACTURED DOOR UNITS: EASYACCESS ® Series 7900: Surface Applied Operator with connecting arms and linkage shall provide positive control of door through entire swing; units shall permit use of butt hung, offset, swing-clear, and center pivot doors.

1. 	Mounting: The operator header shall be mounted to the surface of the existing labeled door frame or wall.

2. 	Door Arms: Connecting hardware shall be a double arm arrangement that can either push the door or pull the door open to suit the job condition. When the operator mounting is on the pull side and a perpendicular wall is within 4" (102 mm) of the door frame, a parallel arm with slide track should be specified.

3. 	Fasteners and Accessories:  Manufacturer's standard corrosion-resistant, non-staining, non-bleeding fasteners and accessories compatible with adjacent materials. UL approved “Fire Exit Hardware” shall be type GXHX as found in the UL Materials Directory. This equipment shall work in conjunction with fire/smoke detection system provided by others.

B. 	EASYACCESS ® HEADER CASE: Shall be a side access extruded aluminum case. Standard header size shall be 4" x 6" (102 mm x 152 mm) with optional 6" x 6" (152 mm x 152 mm).

C. OPERATOR: The Electric Operating Mechanism shall be Series 7000: Operator shall be isolation mounted and concealed in an extruded aluminum case for smooth and quiet operation. Maximum current draw shall not exceed 3.15 amps.

1. 	Opening Action: Shall be accomplished by a 1/15 HP D.C. permanent magnet motor working through reduction gears to the output shaft.

2. 	Field Adjustable Spring Closing Action: shall be accomplished by a field replaceable spring. When the door is in the closing mode or fully closed, motor voltage shall not be required and will be off. The door can be manually operated with power on or off, without damage to the operator and will provide controlled closing.

3.  Independent Adjustable Closing and Latching Speed Control: The operator shall employ independent field adjustment of closing and latching speeds.

4.	Consistent Cycle: The operator shall deliver an even, consistent open force across the entire transition from door fully closed to door open check. Additionally, the range of the force shall be field adjustable to accommodate a wide range of on-site conditions.

5.	Manual Use: The operator shall function as a manual door closer in the direction of swing with or without electrical power.

6.	Controller Protection: The controller shall incorporate the following features to ensure trouble free operation:

a.	Automatic Reset upon power up.

b.	Main fuse and electronic surge protection.

e.	Internal power supply protection.

f.	Resettable sensor supply fuse protection.

8.	Soft Start/Stop: A “soft-start” “soft-stop” motor driving circuit shall be provided for smooth normal opening and recycling.

9.  	Control Switch: Door operators shall be equipped with a three-position function switch to control the operation of the door. Control switch shall provide three modes of operation, Automatic, Off & Hold-Open.

10. 	Master Control: Shall incorporate the following features:

a. 	Adjustable time delay of 2 to 30 seconds (ANSI A156.19 requirement is 5 second minimum time delay).

b. 	Infinite adjustment to opening and open check speeds including adjusting the opening force without affecting the opening speed.

c. 	Immediate reversal of door motion without undue strain on the drive train. This will be accomplished by supplying stepped voltage to the motor. The door shall reverse when closing if an object stops the door.

d. 	Motor Protection Circuit: A locked door motor protection circuit will be supplied that will shut off current to the motor when the door is inadvertently locked or otherwise prevented from opening.

D. OPERATING SEQUENCE (in order of normal use):

1. 	The actuating switch signals the operator when to open. Door closes after time delay expires. Operator to include the following variable adjustments so as to comply with ANSI Standard A156.19: Opening speed - 4 to 6 seconds; Closing speed - 4 to 6 seconds. Opening and closing force, measured 1" (25.4 mm) out from the lock stile of the door, not to exceed 15 pounds (67 N) of force to stop the door when operating in either direction.

2. 	The detection of a fire trips the fire detection device. Provision must be made to remove power from the operator upon activation of the fire alarm causing the door to be mechanically closed by a spring.

3. 	The fire detection device also trips the latch release mechanism on the fire exit hardware causing the latch bolts to engage when the door is in the closed position. The fire exit hardware latches the door closed to contain the fire or smoke and prevent it from spreading to other areas of the building.

4. 	Exiting: The panic bar is depressed which releases the exit device. The springs on the door operator will re-close the door as soon as the door is released. The door will close and re-latch upon reactivation of the fire detection system.

5. 	Reset to automatic mode as required.

2.03  RELATED EQUIPMENT

A.	“KNOWING ACT” ACTIVATING DEVICE: Shall be located on each side of the opening as per ANSI Safety Standard A117 and shall be hardwired to door operator controls.  Activating device shall be momentary contact assembly in one of the following configurations:

1.	PUSHBUTTON: 1" diameter (25 mm) round, red pushbutton switch. Face plates shall be engraved with the international symbol for accessibility and “Press To Open”. Jamb or wall mounted.

2. 	PUSH PLATE: 6" (152 mm) diameter round or 4 ½” (114 mm) square, stainless steel switch. Wall mounted. Optional wireless configuration using radio frequency transmission to receiver located in operator housing.

Optional engravings shall be:

a.	International symbol for accessibility and “Press To Open”.

b.	International symbol for accessibility only.

c.	“Press To Open” only.

d.	Plain - No engraving

3.	TOUCHLESS SENSOR: 1 ¾” (44.5 mm) Jamb-mount, 4 ½” (114 mm) square, or 6” (152 mm) diameter round configurations shall be actuated by waving a hand or solid object in front of sensor surface.

B.	SAFETY DEVICE: Operator shall support non-contact sensors if specified, providing both safety (stop during opening) and recycle (reopen during closing) functions.  Operator shall support monitoring of any presence sensors which support this function. (Sensors not required by ANSI A156.19 Standard for Power Assist and Low Energy Power Operated Swinging Doors.)

C. 	UL LABELED EQUIPMENT: Door, frame, hinges, automatic fire detectors or a central alarm control and “fire exit hardware” type GXHX as found in the UL Building Materials Directory.

2.04  RELATED WORK REQUIREMENTS

A. ELECTRICAL: Provided under Division 16: 120 / 220 VAC, 50/60 Hz, 1 Ø, 5 amp for single operators / 10 amp for dual operators. Non-North American voltages can be 240 VAC (240 volt power supply to be specified for the operator).

B. 	DOOR AND HARDWARE: Labeled door and frame assembly as per NFPA 101 Safety to Life Requirements and NFPA 80 Fire Door Requirements. All hardware used must be UL listed for retarding the spread of fire or smoke

2.05  MATERIALS AND FINISHES

A. 	EXTRUDED ALUMINUM: ASTM B221, 6063-T5 alloy and temper, anodized: Structural Header Sections: Minimum 1/8" (3 mm) thickness.

B. 	FINISHES (for all exposed aluminum surfaces): Shall be one of the following:

1. 	215-R1 Clear: Arch. Class 1 Clear Anodized Coating, AA-MI2C22A41.

2. 	313-R1 Dark Bronze: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

3. 	312-R1 Light Bronze: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

4. 	315-R1 Black: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

5. 	Special Paint Coating: Color as selected.

6. 	Clad with stainless steel or muntz metal (brass alloy): #7 mirror finish or #4 brushed finish.

PART III - EXECUTION

3.01  EXAMINATION

Site Verification of Conditions: Installer must verify that base conditions previously installed under other sections are acceptable for product installation according to manufacturer's instructions. Notify the Contractor in writing of conditions detrimental to the proper and timely completion of work. Do not start work until all negative conditions are corrected in a manner acceptable to the installer and manufacturer.

3.02  INSTALLATION

A. 	GENERAL: Installer shall be factory trained, certified by AAADM, and experienced to perform work in this section. Install door units plumb, level and true to line, without warp or rack of frames or sash with manufacturer's prescribed tolerances. Provide support and anchor in place.

B. 	DISSIMILAR MATERIALS: Comply with AAMA 101, Appendix Dissimilar Materials by separating aluminum materials and other corrodible surfaces from sources of corrosion or electrolytic action contact points.

C. 	WEATHER-TIGHT CONSTRUCTION: Install header and framing members in a bed of sealant or with joint filler or gaskets. Coordinate installation with wall flashings and other components of construction.

D. 	ELECTRICAL: General or electrical contractor to install all wiring to operator on a separate circuit breaker routed into header.

E. SIGNAGE: Signage shall be installed, visible on both sides of the door, in compliance with the requirements of ANSI A156.19 Standard for Power Assist and Low Energy Power Operated Swinging Doors.

3.03  CLEANING, ADJUSTMENT AND PROTECTION

A. 	CLEANING: After installation, installer to take following steps:

1. 	Remove temporary coverings and construction debris from construction site and legally dispose of debris.

3. 	Repair or replace damaged installed products.

4. 	Clean product surfaces and lubricate operating equipment for optimum condition and safety.

B. 	ADJUSTMENT: AAADM certified technician shall inspect & adjust installation for compliance to ANSI A156.19.

C. 	ADVISE CONTRACTOR: Of precautions required through the remainder of the construction period, to ensure that doors will be without damage or deterioration (other than normal weathering) at the time of acceptance.

D.	FIELD QUALITY CONTROL: Testing Services:  Factory Trained Installer shall test and inspect each swinging automatic entrance door to determine compliance of installed systems with applicable ANSI standards.

Note: Horton Automatics reserves the right to make product improvements and change specifications without notice.

## END OF SECTION